## Slide 1: Bio sensor
Ms. D A Chaudhari
H. R. Patel Institute of Pharmaceutical Education and Research, Shirpur

## Slide 3: DEFINITION
Self-contained integrated device that is capable of providing specific qualitative or semi-quantitative analytical information using a biological recognition element which is in direct-spatial contact with a transduction element. (IUPAC,1998)
Biosensor ≠ Bioanalytical System
An Enzyme Electrode is a Biosensor

## Slide 4: CURRENT DEFINITION
A sensor that integrates a biological element with a physiochemical transducer to produce an electronic signal proportional to a single analyte which is then conveyed to a detector.

## Slide 5
Father of Biosensors Leland C. Clark invented the Clark Oxygen Electrode, a pivotal device that allows real-time monitoring of patient’s blood oxygen levels and has made surgery Safer and more successful for millions around the world

## Slide 6: COMPONENTS
Detector

## Slide 8: ELEMENTS OF BIOSENSORS

## Slide 9: BIOSENSOR
Analyte
Sample handling/preparation
Detection
Signal
Analysis
Response

## Slide 10: THE ANALYTE (What do you want to detect?)
Molecule
Protein, toxin, peptide, vitamin, sugar, metal ion
Cholera toxin
Glucose

## Slide 11: SAMPLE HANDLING
(How to deliver the Analyte to the Sensitive Region?)
(Micro) fluidics
Concentration (increase/decrease)
Filtration/selection

## Slide 12: DETECTION/RECOGNITION
(How do you specifically recognize the analyte?)
Fab
Antibody
Enzyme
Active site
Fc
Cell
Membrane receptors
Polymer/Hydrogel
Competitive binding

## Slide 13: SIGNAL (How do you know there was a detection?)
Common Signaling Principles
Optical(SPR,ELM,IR).
Electrical(Voltametry,Potentiometry,
Conductivity).
Electromechanical(QCM
Thermal.
Magnetic.
Pressure.
Often the detector is immobilized on a solid support/sensor.
(The immobilisation permits repeated use of the costly Biological Molecule.)
Specific recognition?

## Slide 14: WORKING PRINCIPLE
Analyte diffuses from the solution to the surface of the Biosensor.
Analyte reacts specifically & efficiently with the Biological Component of the Biosensor.
This reaction changes the physicochemical properties of the Transducer surface.
This leads to a change in the optical/electronic properties of the Transducer Surface.
The change in the optical/electronic properties is measured/converted into electrical signal, which is detected.

## Slide 15: BASIC CHARACTERESTICS
detection of High
LINEARITY : Should be High – For the Substrate Concentration.
SENSITIVITY : Value of Electrode Response per Substrate Concentration.
SELECTIVITY : Chemical Interference must be minimized for obtaining Correct Result.
RESPONSE TIME :Time necessary for having 95% of the Response.

## Slide 16: ADVANTAGES
Highly Specific.
Independent of Factors like stirring, pH, etc. Linear response, Tiny & Biocompatible.
Easy to Use, Durable.
Require only Small Sample Volume. Rapid, Accurate, Stable & Sterilizable.

## Slide 17: TYPICAL SENSING TECHNIQUES
🠶Fluorescence.
🠶DNA Microarray.
🠶SPR (Surface Plasma Resistance).
🠶Impedance Spectroscopy.
🠶SPM (Scanning Probe Microscopy, AFM, STM).
🠶QCM (Quartz Crystal Microbalance).
🠶SERS (Surface Enhanced Raman Spectroscopy).
🠶Electrochemical.

## Slide 18: TYPES
Calorimetric/Thermal Detection Biosensors.
Optical Biosensors.
Resonant Biosensors.
Piezoelectric Biosensors.
Ion Sensitive Biosensors.
Electrochemical Biosensors.
  Conductimetric Sensors.
Amperometric
Potentiometric
Sensors. Sensors.

## Slide 19
Calorimetric / Thermal Detection Biosensors.
  Uses Absorption / Production of Heat.
  Total heat produced/absorbed is ᾶ Molar Enthalpy/Total No. of molecules in the rn.
Temp. measured by Enzyme Thermistors.
Advantages:
No need of Frequent recalibration.
Insensitive to the Optical & Electrochemical Properties of the sample.
Uses:
Detection of: (1) Pesticides .
(2) Pathogenic Bacteria.

## Slide 20
Optical Biosensors.
  Colorimetric for colour - Measures change in
Light Adsorption.
  Photometric for Light Intensity - Detects the
Photon output.
Resonant Biosensors.
  An Acoustic Wave Transducer is coupled with
Bioelement.
    Measures the change in Resonant Frequency.

## Slide 21
Piezoelectric Biosensors.
Uses Gold - To detect specific angle at which ȇ waves are emitted when the substance is exposed to laser light/crystals like quartz, which vibrates under the
influence of an electric field.
Change in Frequency ᾶ Mass of Absorbed material.
Ion Sensitive Biosensors.
  Are semiconductor FETs with ion-sensitive surface.
Surface Electrical Potential changes when the ions &
semiconductors interact.
  Measures the Change in Potential.
Uses:
o pH Detection.

## Slide 22
Electrochemical Biosensors.
Underlying Principle – Many chem.rns produce or consume ions or ȇs causing some change in the elctrical properties of the solution that can be sensed out & used as a measuring parameter.
Uses:
Detection of :
Hybridized DNA
DNA- binding Drugs &
Glucose Concentration.
Conductimetric Sensors.
  Measures Electrical Conductance/Resistance of the
solution.

## Slide 23
Conductance Measurements have relatively Low
Sensitivity.
Electrical Field is generated using sinusoidal(ac) voltage, which helps in minimizing undesirable effects
like:
i. Faradaic processes. Double layer charging &
ii.
iii. Concentration polarization.
Amperometric Biosensors.
  High Sensitivity Biosensor.
Detects electroactive species present in the
biological test samples.
  Measured Parameter – Current.

## Slide 24
Potentiometric Sensors.
Working Principle – When ramp voltage is applied to an electrode in solution, a current flow occurs
because of electrochemical reactions.
  Measured Parameter – Oxidation / reduction Potential of an Electrochemical rn.

## Slide 28: APPLICATIONS

## Slide 29
Food Analysis.
Study of Biomolecules & their Interaction.
Drug Development.
Crime Detection.
Medical Diagnosis (Clin&Lab).
Environmental Field Monitoring.
Quality Control.
Industrial Process Control.
Detection Systems for Biological Warfare Agents.
Manf. Of Pharmaceuticals & Replacement organs.

## Slide 30: BIOSENSOR FOR AGRICULTURAL & FOOD INDUSTRY
Detection of viral, fungal, bacterial diseases of plants.
In food industry, detection of total microbes & food quantification in soft drinks.
To determine the freshness of other fish, beef & other food items.
Makes Bacteria GLOW by OPTICAL Biosensor

## Slide 32
The DNA capture element instrument- for hereditary diseases
Glucometer- for measurement of glucose in blood.

## Slide 33
Pregnancy Test.
Detects the hCG protein in urine.
Interpretation and data analysis
performed by the user.
Infectious Disease Biosensor.
Data analysis and interpretation performed by a microprocessor.

## Slide 34
Old time coal miners’ Biosensor
Data analysis and interpretation performed by the coal miner.

## Slide 35: BIOSENSOR FOR DETECTION OF POLLUTION & OF THE CHEMICALS PRESENT IN THE ENVIRONMENT